## Slide 1: RISC-V

## Slide 2: Eight Great Ideas
Design for Moore’s Law
Use abstraction to simplify design
Make the common case fast
Performance via parallelism
Performance via pipelining
Performance via prediction
Hierarchy of memories
Dependability via redundancy

## Slide 3: Below Your Program
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers

## Slide 4: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 5: Why RISC V?
Silicon vendors look for ways to innovate, reduce costs and stay ahead of the competition, many are now turning to RISC-V, the open standard instruction set architecture (ISA).
RISC-V is enabling a new, collaborative era of processor innovation.
Because it’s open standard, architects, designers and developers can modify and improve upon the existing ISA codebase as needed.
This flexibility has allowed teams to experiment with architectures and chip designs within the same ISA and has enabled a collaborative environment

## Slide 6: History of RISC-V.
The development of the RISC-V standard began in 2010 when researchers at the University of California, Berkeley created a simple, yet powerful ISA that could be used by anyone with minimal restrictions.
It was released in 2015 as a free and open-standard ISA that allows anyone to design, manufacture and sell processors based on the RISC-V specification — without royalties or license fees.
Now managed by the RISC-V Foundation (riscv.org)

## Slide 7: Industry Opinion about RISC V & Applications
RISC-V has grown rapidly due to its flexibility and cost-saving benefits because it can be an ideal way to customize computing environments without the high costs of proprietary ISA’s.
These advantages are quickly being recognized across industries, and businesses have been taking advantage of RISC-V cores for all kinds of applications including LINK
  Artificial intelligence (AI) image sensors,
  Security management,
  AI computing,
  Machine control systems for 5G networks, and
  More sophisticated storage, graphics and machine learning applications.

## Slide 9: Advantage of RISC V
The 3 main advantages of RISC-V
Flexibility: RISC-V offers a unique set of features that allow users to customize and optimize both software and hardware for specific use cases, resulting in faster development cycles and better design tradeoffs for performance, power and area.
Control: This open ISA provides designers and developers with greater control over their computing environments, allowing them to fine-tune their systems without relying on third parties or incurring additional license fees associated with proprietary architectures.
Visibility: The open-standard nature of RISC-V also means that developers have more visibility into the codebase, making it easier to understand the roadmap and identify potential security risks before they become an issue.

## Slide 10: ARM vs RISC V : ISA Comparison
ISAs can be broadly categorized into two types:
Open ISA
Closed ISA
  Closed ISAs, like ARM, are proprietary and tightly controlled by specific companies (Arm Holdings here), offering established reliability and compatibility but limiting customization.
  Open ISAs, exemplified by RISC-V, are community-driven and provide greater flexibility for customization, fostering innovation and adaptation to specific needs.

## Slide 11: ARM vs RISC V : Architectural Overview
16bit compressed instruction is decompressed into 32bit Instruction

## Slide 12: ARM vs RISC V : Performance
In the performance comparison between RISC-V and ARM,
ARM's consistent iteration, comprehensive ecosystem, and wide range of options give it a notable performance advantage.
However, RISC-V's modular nature and customization potential hold promise for specific use cases. The ongoing efforts of RISC-V proponents to narrow the performance gap will be a crucial factor in determining how well RISC-V can match ARM's established performance standards in the future.

## Slide 13: ARM vs RISC V : Power Efficiency
ARM's refined power management techniques and specialized cores give it a major advantage in power efficiency.
While RISC-V holds promise due to its customization potential, its open nature requires a more extensive investment of time and resources to fully harness its energy-saving capabilities.

## Slide 14: RISC V Architecture
The RISC-V architecture is based on the RISC principles (as compared to CISC), which emphasize a small, simple, and efficient instruction set.
  The key architectural features of RISC-V include
  load-store architecture
  fixed-length 32-bit instruction format
  small number of general-purpose registers
  RISC-V supports various integer instruction set extensions, such as RV32I (32-bit), RV64I (64-bit), and RV128I (128-bit), which define the base integer instruction set for different address space sizes.
  RISC-V utilizes little-endian byte ordering within the memory system, implying that the smallest significant byte of multi-byte data is stored at the lowest memory address.

## Slide 15: RISC V Architecture: Modularity & Extensibility
One of the defining characteristics of RISC-V is its modularity and extensibility.
The ISA is designed to be easily extended with custom instructions and coprocessors, allowing for tailored implementations that meet specific application requirements.
This flexibility is achieved through a modular design, where the base ISA can be combined with optional standard extensions, such as the M extension for integer multiplication and division, the A extension for atomic operations, and the F and D extensions for single- and double-precision floating-point arithmetic.

## Slide 16: Standard extensions
Standard RISC encoding in a fixed 32- bit instruction format
The “C” extension (compressed extension) offers shorter 16-bit versions of common 32-bit RISC-V instructions (can be intermixed with 32-bit instructions)
Do not confuse C extension with C programming language!

## Slide 17: RISC V Architecture: Compressed Instruction set
Compared to ARM’s Thumb instruction set, RISC-V also supports a compressed instruction set extension called RV32C (or RV64C for 64-bit), which provides 16-bit compressed instructions that can be mixed with the standard 32-bit instructions.
This feature helps reduce code size and improve energy efficiency, making RISC-V particularly suitable for embedded systems and low-power applications.

## Slide 18: 2 Versions of RISC-V (based on maximum width of registers supported)
RISC-V 32 (RV32): max register width (XLEN) is 32 bits
RISC-V 64 (RV64): max register width (XLEN) is 64 bits
RV64 supports RV32 also.
Both versions have 32 registers.
In both of them, each instruction is encoded into 32 bits.
Register file
32-bit in RV32 64-bit in RV64
…
x0 x1 x2 x3 x4 x5
x31

## Slide 19: RISC V Modes: Privilege levels & Virtual Memory
The RISC-V Privileged Architecture Specification defines three privilege levels:
  machine mode (M-mode),
  supervisor mode (S-mode),
  user mode (U-mode).
These privilege levels provide a mechanism for isolating the operating system kernel, hypervisors, and user applications, ensuring system security and stability.
RISC-V also supports a virtual memory system based on a multi-level page table scheme, enabling efficient memory management and protection.

## Slide 20: RISC-V Modes
RISC-V Privileged Specification defines 3 levels of privilege, called Modes
Machine mode is the highest privileged mode and the only required mode
  Flexibility allows for a range of targeted implementations from simple MCUs to high- performance Application Processors
  Example for Simple bare metal application Machine mode is enough and it’s the default and mandatory mode, for an isolation boundary between the application and more direct hardware access, M and U mode may both be supported.
  A robust system, such as a server or desktop machine will support M, S, and U as the Supervisor mode will bring the benefits of Virtualization and Hypervisor called Hypervisor-extended Supervisor (HS)
Machine, Hypervisor, Supervisor modes each have Control
and Status Registers (CSRs)
RISC-V Modes |  | 
Level | Name | Abbr.
0 | User/Application | U
1 | Supervisor | S
2 | Hypervisor | HS
3 | Machine | M
Supported Combinations of Modes | 
Supported Levels | Modes
1 | M
2 | M, U
3 | M, S, U
4 | M, HS, S, U

## Slide 21: We will discuss 4 addressing modes (relevant for RISC-V)
Immediate
Register direct
Register indirect
Base-offset
NOTE: Register indirect is a special case of base-offset. If we set offset as zero, we get register indirect mode

## Slide 22: 1. Immediate addressing mode
imm
value
Value ← imm
The value (e.g., 4, 8, 0x13, -3 etc) is available in the instruction itself. No need to access register file

## Slide 23: 2. Register Direct Mode
Value ← r1
186 | 
784 | 
410 | 
r1
register file
value
r0 r1
r15
The value is obtained from the register directly.
784

## Slide 24: Examples of instructions that use those modes
Register direct: sub r3, r1, r2
r1 and r2 values are fetched from registers. Result is stored in r3
Immediate: addi r3, r1, 500
Here, r1 and r3 are accessed from registers and 500 is the immediate value available in the instruction itself.
RISC-V: at most one operand can be an immediate.

## Slide 25: 3. Register Indirect Mode
Value ← (r1)
148 | 
r1 r0
4019
register file
Memory
value
Read value of r1 from register file. This gives a memory address
Read the value stored in memory at that address
r1
r15
0
4
100
148
4019

## Slide 26: 4. Base-offset Addressing Mode
Value ← offset(r1)
451 | 
r1 r0
8914
register file
memory
value
offset
r1
r15
Read value of r1 from register file. Add offset to it. This gives a memory address
Read the value stored in memory at that address
Let offset = 9
0
4
100
460
8914

## Slide 27: Examples of instructions that use those modes
r1
r2
register
file
lw r1, 10(r2)
memory
10
r1
r2
register
file
sw r1, 10(r2)
memory
10
(a)
(b)
Load and store instructions use register indirect and base-offset addressing modes
Lw = load word
Sw= store word

## Slide 28: Solved Example
Consider below instructions that are executed when the state of register file and memory is as given here.
ld x6, 24(x10)
sd x5, 16(x10)
Show only the changed values in RF and memory after these instructions are executed.
Solution: x10+24 is 1040. ld instruction will load from 1040 and store that value in register x6. So, x6 will become 67891234
x10+16 is 1032. sd instruction will store the value of x5 at address 1032. Hence, memory address 1032 will change to 3897409

## Slide 29: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c // a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost

## Slide 30: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled RISC-V code:
add t0, g, h // temp t0 = g + h add t1, i, j // temp t1 = i + j sub f, t0, t1 // f = t0 - t1

## Slide 31: Register Operands
Arithmetic instructions use register operands
RISC-V has a count of 32 registers having a width (64-bit or 32bit)
  Use for frequently accessed data
  64-bit data is called a “double word”
    32 x 64-bit/32-bit general purpose registers x0 to x31
  32-bit data is called a “word”
Design Principle 2: Smaller is faster
  Compact flash main memory: millions of locations

## Slide 32: RISC-V Registers
x0: the constant value 0
x1: return address
x2: stack pointer
x3: global pointer
x4: thread pointer
x5 – x7, x28 – x31: temporaries
x8: frame pointer
x9, x18 – x27: saved registers
x10 – x11: function arguments/results
x12 – x17: function arguments

## Slide 33: RISC-V Registers
RV32I/64I have 32 Integer Registers
  Optional 32 FP registers with the F and D extensions
  RV32E reduces the register file to 16
integer registers for area constrained embedded devices
Width of Registers is determined by ISA
RISC-V Application Binary Interface (ABI)
defines standard functions for registers
  Allows for software interoperability
Development tools usually use ABI names for simplicity
Register | ABI Name | Description | Saver
x0 | zero | Hard-wired zero | -
x1 | ra | Return address | Caller
x2 | sp | Stack pointer | Callee
x3 | gp | Global pointer | -
x4 | tp | Thread pointer | -
x5-7 | t0-2 | Temporaries | Caller
x8 | s0/fp | Saved register/Frame pointer | Callee
x9 | s1 | Saved register | Callee
x10-11 | a0-1 | Function Arguments/return values | Caller
x12-17 | a2-7 | Function arguments | Caller
x18-27 | s2-11 | Saved registers | Callee
x28-31 | t3-6 | Temporaries | Caller

## Slide 34: Register Description
Register x0 RISC-V dedicates register x0 to be hard-wired to the value zero.
Return address A link to the calling site that allows a procedure to return to the proper address; in RISC-V it is stored in register x1.
Program counter(PC) The register containing the address of the instruction in the program being executed.
Stack pointer A value denoting the most recently allocated address in a stack that shows where registers should be spilled or where old register values can be found. In RISC-V, it is register sp, or x2.
Global pointer The register that is reserved to point to the static area where static variables are stored.
Frame pointer A value denoting the location of the saved registers and local variables for a given procedure.
Argument registers: x10 to x17 are used to pass arguments to a function. Before calling a function, arguments are copied to these registers. If more than 8 arguments need to be passed, we use the stack.
Temporary registers (t0 to t6): used to hold intermediate values during instruction or function execution.
Thread-pointer register, tp, that is designed for thread-local data.

## Slide 35: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in x19, x20, …, x23
Compiled RISC-V code:
add x5, x20, x21 add x6, x22, x23 sub x19, x5, x6

## Slide 36: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
RISC-V is Little Endian
  Least-significant byte at least address of a word
  c.f. Big Endian: most-significant byte at least address
RISC-V does not require words to be aligned in memory
  Unlike some other ISAs
What is XLEN in RISC-V?
RISC-V is little-endian and comes in 32 and 64 bit flavours. In keeping with the RISC-V documents, the flavour (either 32 or 64) is called XLEN in further slides at few places where it matters.

## Slide 37: Memory Operand Example
C code:
A[12] = h + A[8];
  h in x21, base address of A in x22
Compiled RISC-V code:
  Index 8 requires offset of 32
    4 bytes per word
ld x9, 32(x22) add x9, x21, x9 sd x9, 48(x22)

## Slide 38: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 39
Although the RISC-V registers in this course are 32 bits wide, the RISC-V architects conceived multiple variants of the ISA.
In addition to this variant, known as RV32, a variant named RV64 has 64-bit registers, whose larger addresses make RV64 better suited to processors for servers and smart phones.
RV32 and RV64

## Slide 40: Immediate Operands
Constant data specified in an instruction
addi x22, x22, 4
Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 41: Example on add
Mapping of variables
i x19, g x20
to registers:
C codes | C code (simplified) | RISC-V code
i++ | i++ | addi x19, x19, 1
g = ++i | i++ g=i | addi x19, x19, 1 add x20, x19, x0
g = i++ | g=i i++ | add x20, x19, x0 addi x19, x19, 1

## Slide 42: LI and MV (pseudo) instructions
Load Immediate (LI) loads register rd with an immediate value
Syntax: li rd, imm
li t0, 0x4A
mv t1, t0
# Load register t0 with a value
# Copy contents of register t0 to register t1
Pseudo instructions are similar to macros in C/C++.
C codes | RISC-V code
v= 10 | li t0, 10
v=r | mv t0, t1
Assuming v and r are stored in t0 and t1, respectively.

## Slide 43: RISC-V R-format Instructions
Instruction fields
  opcode: operation code
  rd: destination register number
  funct3: 3-bit function code (additional opcode)
  rs1: the first source register number
  rs2: the second source register number
  funct7: 7-bit function code (additional opcode)
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits

## Slide 44: R-format Example
add x9,x20,x21
0000 0001 0101 1010 0000 0100 1011 0011two =
015A04B316
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
0
21
20
9
0
51
0000000
10101
10100
01001
000
0110011

## Slide 45: RISC-V I-format Instructions
Immediate arithmetic and load instructions
  rs1: source or base address register number
  immediate: constant operand, or offset added to base address
    2s-complement, sign extended
Design Principle 3: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits

## Slide 46: RISC-V S-format Instructions
Different immediate format for store instructions
  rs1: base address register number
  rs2: source operand register number
  immediate: offset added to base address
    Split so that rs1 and rs2 fields always in the same place
rs2
rs1
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
imm[11:5]
imm[4:0]

## Slide 47: The 6 Instruction Formats
R-Format: instructions using 3 register inputs
  add, xor, mul —arithmetic/logical ops
I-Format: instructions with immediates, loads
  addi, lw, jalr, slli
S-Format: store instructions: sw, sb
SB-Format: branch instructions: beq, bge
U-Format: instructions with upper immediates
  lui, auipc —upper immediate is 20-bits
UJ-Format: jump instructions: jal

## Slide 48: Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | RISC-V
Shift left | << | << | slli
Shift right | >> | >>> | srli
Bit-by-bit AND | & | & | and, andi
Bit-by-bit OR | ¦ | ¦ | or, ori
Bit-by-bit XOR | ^ | ^ | xor, xori
Bit-by-bit NOT | ~ | ~ | 
Useful for extracting and inserting groups of bits in a word

## Slide 49: Shift Operations
immed: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  slli by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srli by i bits divides by 2i (unsigned only)
rs1
rd
funct3
opcode
6 bits
7 bits
5 bits
5 bits
3 bits
funct6
immed
6 bits

## Slide 50: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs1, rs2, L1
  if (rs1 == rs2) branch to instruction labeled L1
bne rs1, rs2, L1
  if (rs1 != rs2) branch to instruction labeled L1

## Slide 51: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in x19, x20, …
Compiled RISC-V code:
bne x22, x23, Else add x19, x20, x21 beq x0,x0,Exit // unconditional Else: sub x19, x20, x21 Exit: …
Assembler calculates addresses

## Slide 52: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in x22, k in x24, address of save in x25
Compiled RISC-V code:
Loop: slli x10, x22, 3 add x10, x10, x25 ld x9, 0(x10) bne x9, x24, Exit
addi x22, x22, 1 beq x0, x0, Loop Exit: …
C code | Simplified C code | RISC-V code
Arr[i] =5; | temp=5 Offset = i*8 addr = Arr + offset Memory[addr] = temp | li a3, 5 slli a4, a1, 3 add a5, a4, a0 sd a3, 0(a5)
val = Arr[7] |  | ld a2, 56(a0)
Assume “long int” variables (8B).
Base address of Arr is in a0. i is in a1. val is in a2

## Slide 53: More Conditional Operations
blt rs1, rs2, L1
  if (rs1 < rs2) branch to instruction labeled L1
bge rs1, rs2, L1
  if (rs1 >= rs2) branch to instruction labeled L1
Example
  if (a > b) a += 1;
  a in x22, b in x23
  bge x23, x22, Exit // branch if b >= a
  addi x22, x22, 1
  Exit:

## Slide 54: Signed vs. Unsigned
A number stored in a register or memory address can be interpreted as signed (2’s complement) or unsigned. Both may lead to different decimal numbers.
  x22 = 1111 1111 1111 1111 = 65535 (unsigned), -1 (signed)
  x23 = 0000 0000 0000 0001 = 1 (signed), 1 (unsigned)
  On comparing them, result depends on whether you take them as signed or unsigned.
  On signed comparison, x22<x23 because -1 < +1
  On unsigned comparison, x22 > x23 because +65535 > +1

## Slide 55: Signed and unsigned comparison
To take this into account, RISC-V has two variants of comparison/branching instructions.
Signed comparison: blt, bge
Unsigned comparison: bltu, bgeu

## Slide 56: SLT:SET On Less Than (signed comparison) and SLTU (unsigned comparison)
Syntax: slt rd, rs1, rs2
SLT writes 1 to rd if rs1 < rs2, 0 otherwise. Example code:
li x5, 39 | # x5 |  39
li x3, 57 | # x3 |  57
slt x1, x5, x3 | # x1 |  x5 < x3. So, x1 will store 1
C code | RISC-V code
if (a<b) c=1; else c=0; | slt a2, a0, a1
Assuming a/b/c are stored in
a0/a1/a2 respectively.

## Slide 57: Comparison Instructions (SLT and SLTU)
li a0, -4
li a1, 3
slt a2, a0, a1 sltu a3, a0, a1
# a0  0xFFFFFFFC (in hex)
# a1  3
# a2  1 because -4<3 is true
# a3  0 because 0xFFFFFFFC <3 is False
li a0, 4
li a1, -3
slt a4, a0, a1 sltu a5, a0, a1
# a0  4
# a1  0xFFFFFFFD
# a4  0 because 4<-3 is false
# a5  1 because 0x4< 0xFFFFFFFD is true
SLT and SLTU perform signed and unsigned compares respectively, writing 1 to rd if rs1 < rs2, 0 otherwise.

## Slide 58: Variants of SLT
SEQZ: Set If Equal to Zero . Example: seqz x6, x5
Syntax: seqz rd, rs1
If x5 was zero, then x6 is set to 1. Otherwise, x6 is set to 0.
Similar instructions:
SGTZ: Set If Greater Than Zero SLTZ: Set If Less Than Zero
SNEZ: Set If Not Equal to Zero
C code | RISC-V code
if (a==0) c=1; else c=0; | seqz a2, a0
Assuming a/b/c are stored in a0/a1/a2 respectively.

## Slide 60: Procedure Calling
Steps required
  Place parameters in registers x10 to x17
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call (address in x1)
Caller
The program that instigates a procedure and provides the necessary parameter values.
Callee
A procedure that executes a series of stored instructions based on parameters provided by the caller and then returns control to the caller.

## Slide 61: Procedure Call Instructions
Procedure call: Jump and link
jal x1, ProcedureLabel
  Address of following instruction put in x1
  Jumps to target address ProcedureLabel
Procedure return (Also a Pseudo Instruction):
ret
  Jumps to address in x1
  ret is same as “jalr x0, x1, 0”
Jump and link register
jalr x0, 0(x1)
  Like jal, but jumps to 0 + address in x1
  Use x0 as rd (x0 cannot be changed)

## Slide 62: How to pass arguments/ return values
Solution : use registers
.func:
add a0, a0, a1 ret
.main:
li a0, 3
li a1, 5
jal x1, .func add a2, a0, 10
Before calling a function, arguments
are copied to registers a0 and a1.
a0 is same as x10 a1 is same as x11
Return value is stored in a0 itself

## Slide 63: Limitations with use of registers for argument passing or returning results
Space Problem
  We have a limited number of registers
  We cannot pass more than certain number of arguments
  Solution : Use memory also
Overwrite Problem
  What if a function calls itself ? (recursive call)
  The callee can overwrite the registers of the caller
  Solution : Spilling
  Note: spilling is a technique in which, a variable is moved out from a register space to the main memory(the RAM) to make space for other variables, which are to be used in the program currently under execution.

## Slide 64: Register Spilling
caller saved scheme
  The caller can save the set of registers its needs
  Call the function
  And then restore the set of registers after the function returns
  Known as the caller saved scheme
callee saved scheme
  The callee saves the registers, and later restores them

## Slide 65: caller or callee-saver conventions
Saver is “caller”: means that a function caller must save that register somewhere before calling e.g. main()
Saver is “callee”: means that if a function wants to use that register, it
must first save it somewhere, and restore it before returning e.g. add()
Save registers
Restore registers
Callee
Caller
Callee
Save registers
Restore registers
Caller
(a)
(b)
Caller saved
Callee saved

## Slide 66: Limitations with our approach
17
Using memory, and spilling solves both the space problem and overwrite problem
However, there needs to be :
  a strict agreement between the caller and the callee regarding the set of memory locations that need to be used
  Secondly, after a function has finished execution, all the space that it uses needs to be reclaimed

## Slide 67: Activation Block
Activation block → memory map of a function
arguments, register spill area, local variables
int foo(int arg1) {
int a, b, c;
a = 3; b = 4;
c = a + b + arg1; return c;
}
Activation block
Arguments
Return address
Register spill area
Local variables

## Slide 68: Organising Activation Blocks
All the information of an executing function is stored in its activation block
These blocks need to be dynamically created and destroyed – millions of times
What is the correct way of managing them, and ensuring their fast creation and deletion ?
Is there a pattern ?

## Slide 69: Pattern of Function Calls
foo
main
test
test2
foobar
foobarbar
main() {
test();
foo();
}
test() {
...
test2(); return;
}
test2() {
...
return;
}
foo() {
...
foobar(); return;
}
foobar() {
...
foobarbar(); return;
}
foobarbar() {
...
return;
}

## Slide 70: Pattern of Function Calls
21
•
Last in First Out
Use a stack to store activation blocks
Stack
foo
foo
foobar
foo
foobar
foobarbar
foo
foobar
(a)
(b)
(c)
(d)

## Slide 71: Issues solved by stack
22
Space problem
  Pass as many parameters as required in the activation block
Overwrite problem
  Solved by activation blocks
Management of activation blocks
  Solved by the notion of the stack

## Slide 72: Working with the Stack
Allocate a part of the memory to save the stack
Traditionally stacks are downward growing.
  The first activation block starts at the highest address
  Subsequent activation blocks are allocated lower addresses
The stack pointer register (sp) points to the beginning of an activation block
Allocating an activation block : sp ← sp - <constant>
De-allocating an activation block: sp ← sp + <constant>
23

## Slide 73
myFunction:
addi sp,sp,-24
sd x5,16(sp)
sd x6,8(sp)
sd x20,0(sp) add x5,x10,x11
add x6,x12,x13
sub x20,x5,x6
addi x10,x20,0 ld x20,0(sp)
ld x6,8(sp)
ld x5,16(sp) addi sp,sp,24 ret
Saving variable in stack (pushing and popping)
Save x5, x6, x20 on stack (called pushing)
Resore x5, x6, x20 from stack (called popping)
Return to caller
This is an example of callee saved scheme
Do some processing of a function

## Slide 74: How Stack Functions
Stack grows downwards

## Slide 75: A Question on Stack
1011
1012
1013
1014
1015
1016
1017
1018
1019
1020
1021
1022
1023
1024
1025
1026
?
?
?
?
?
?
?
?
Byte addresses
Consider 32b version of RISC-V and see below code.
addi sp,sp,-12 sw x5,8(sp) sw x6,4(sp) sw x20,0(sp)
Initially, we have value of
x5 as 0x12345678, x6 as 0xABCDEF09 x20 as 0xACE02468.
sp is 1024.
In this figure, write the values shown by ?

## Slide 76: Solution
1011
1012
1013
1014
1015
1016
1017
1018
1019
1020
1021
1022
1023
1024
1025
1026
68
24
E0
AC
09
EF
CD
AB
78
56
34
12
Byte addresses
(a) Little Endian
1011
1012
1013
1014
1015
1016
1017
1018
1019
1020
1021
1022
1023
1024
1025
1026
AC
E0
24
68
AB
CD
EF
09
12
34
56
78
Byte addresses
(b) Big Endian
RISC-V is little endian
Hence, (a) is correct for RISC-V
(b) is correct for any Big-endian ISA

## Slide 77: Leaf Procedure Example
C code:
long long int leaf_example ( long long int g, long long int h, long long int i, long long int j) { long long int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j in x10, …, x13
  f in x20
  temporaries x5, x6
  Need to save x5, x6, x20 on stack

## Slide 78: Leaf Procedure Example
RISC-V code:
leaf_example:
addi sp,sp,-24
sd x5,16(sp)
sd x6,8(sp)
sd x20,0(sp
add x5,x10,x11
add x6,x12,x1
sub x20,x5,x6
addi x10,x20,0
ld x20,0(sp)
ld x6,8(sp)
ld x5,16(sp)
addi sp,sp,24
jalr x0,0(x1)
Save x5, x6, x20 on stack
x5 = g + h
x6 = i + j
f = x5 – x6
copy f to return register
Resore x5, x6, x20 from stack
Return to caller

## Slide 79: Register Usage
x5 – x7, x28 – x31: temporary registers
  Not preserved by the callee
x8 – x9, x18 – x27: saved registers
  If used, the callee saves and restores them
What is and what is not preserved across a procedure call

## Slide 80: Byte/Halfword/Word Operations
RISC-V byte/halfword/word load/store
  Load byte/halfword/word: Sign extend to 64 bits in rd
    lb rd, offset(rs1)
    lh rd, offset(rs1)
    lw rd, offset(rs1)
  Load byte/halfword/word unsigned: Zero extend to 64 bits in rd
    lbu rd, offset(rs1)
    lhu rd, offset(rs1)
    lwu rd, offset(rs1)
  Store byte/halfword/word: Store rightmost 8/16/32 bits
    sb rs2, offset(rs1)
    sh rs2, offset(rs1)
    sw rs2, offset(rs1)

## Slide 81: RISC-V SB-format Instructions: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
SB format:
PC-relative addressing
  Target address = PC + immediate × 2
rs2
rs1
funct3
opcode
imm [10:5]
imm [4:1]
imm[12]
imm[11]

## Slide 82: RISC-V UJ-format Instructions : Jump Addressing
Jump and link (jal) target uses 20-bit immediate for larger range
UJ format:
For long jumps, eg, to 32-bit absolute address
  lui: load address[31:12] to temp register
  jalr: add address[11:0] and jump to target
rd
opcode
7 bits
5 bits
imm[11]
imm[20]
imm[10:1]
imm[19:12]

## Slide 83: RISC-V Addressing Summary

## Slide 84: RISC-V Encoding Summary

## Slide 85: RISC-V Multiplication
Four multiply instructions:
  mul: multiply
    Gives the lower 64 bits of the product
  mulh: multiply high
    Gives the upper 64 bits of the product, assuming the operands are signed
  mulhu: multiply high unsigned
    Gives the upper 64 bits of the product, assuming the operands are unsigned
  mulhsu: multiply high signed/unsigned
    Gives the upper 64 bits of the product, assuming one operand is signed and the other unsigned
  Use mulh result to check for 64-bit overflow

## Slide 86: RISC-V Division
Four instructions:
  div, rem: signed divide, remainder
  divu, remu: unsigned divide, remainder
Overflow and division-by-zero don’t produce errors
  Just return defined results
  Faster for the common case of no error

## Slide 87
CSR and ECALL Instructions
Control and Status Registers (CSRs) have their own dedicated instructions :
  Read/Write
  Read and Set bit
  Read and Clear bit
Environment Call instruction used to transfer control to the execution environment and a higher privileged mode
  Triggers a synchronous Interrupt (discussed later)
  Example: User mode program can use an ECALL to transfer control to a Machine mode OS kernel, aka System Call

## Slide 88: What are Control and Status Registers (CSRs)
CSRs are Registers which contain the working
state of a RISC-V machine
CSRs are specific to a Mode
  Machine Mode has ~17 CSRs (not including performance monitor CSRs)
  Supervisor Mode has a similar number, though most are subsets of their equivalent Machine Mode CSRs
    Machine Mode can also access Supervisor CSRs
CSRs are defined in the RISC-V privileged specification
  We will cover a few key CSRs here

## Slide 89: Identification CSRs
misa – Machine ISA Register
  Reports the ISA supported by the hart (i.e. RV32bit , 64bit, 128bit)
mhartid – Machine hart/Core ID
  Integer ID of the Hardware Thread (Core)
mvendorid – Machine Vendor ID
  JEDEC Vendor ID
marchid – Machine Architecture ID
  Used along with mvendorid to identify a implementation. No format specified
mimpid - Machine Implementation ID
  Implementation defined format
Note: In RISC V Architecture we call Core as hart(hardware Thread)

## Slide 90: Machine Status (mstatus) - The Most Important CSR
Control and track the hart’s current operating state
Bits | Field Name | Description
0 | UIE | User Interrupt Enable
1 | SIE | Supervisor Interrupt Enable
2 | Reserved | 
3 | MIE | Machine Interrupt Enable
4 | UPIE | User Previous Interrupt Enable
5 | SPIE | Supervisor Previous Interrupt Enable
6 | Reserved | 
7 | MPIE | Machine Previous Interrupt Enabler
8 | SPP | Supervisor Previous Privilege
[10:9] | Reserved | 
[12:11] | MPP | Machine Previous Privilege
Bits | Field Name | Description
[14:13] | FS | Floating Point State
[16:15] | XS | User Mode Extension State
17 | MPRIV | Modify Privilege (access memory as MPP)
18 | SUM | Permit Supervisor User Memory Access
19 | MXR | Make Executable Readable
20 | TVM | Trap Virtual memory
21 | TW | Timeout Wait (traps S-Mode wfi)
22 | TSR | Trap SRET
[23:30] | Reserved | 
[31] | SD | State Dirty (FS and XS summary bit)
RV32 mstatus CSR

## Slide 91: Timer CSRs
mtime
  RISC-V defines a requirement for a counter exposed as a memory mapped register
  There is no frequency requirement on the timer, but
    It must run at a constant
frequency
    The platform must expose frequency
Bits | Field Name | Description
[63:0] | mtime | Machine Time Register
Bits | Field Name | Description
[63:0] | mtimecmp | Machine Time Compare Register
mtime CSR
mtimecmp CSR
mtimecmp
  RISC-V defines a memory mapped timer compare register
  Triggers an interrupt when mtime is greater than or equal to mtimecmp

## Slide 92: Supervisor CSRs
Most of the Machine mode CSRs have Supervisor mode equivalents
– Supervisor mode CSRs can be used to control the state of Supervisor and User Modes.
Most equivalent Supervisor CSRs have the same mapping as Machine mode without Machine mode control bits
sstatus, stvec, sip, sie, sepc, scause, satp, and more
satp - Supervisor Address Translation and Protection Register
– Used to control Supervisor mode address translation and protection
– Virtual Memory is only supported in Supervisor mode
Bits | Field Name | Description
[21:0] | PPN | Physical Page Number of the root page table
[30:22] | ASID | Address Space Identifier
31 | MODE | MODE=1 uses Sv32 Address Translation
RV32 satp CSR
Bits | Field Name | Description
[43:0] | PPN | Physical Page Number of the root page table
[59:44] | ASID | Address Space Identifier
[63:60] | MODE | Encodings for Sv32, Sv39, Sv48
RV64 satp CSR

## Slide 93: Virtual Memory
RISC-V has support for Virtual Memory allowing for sophisticated memory management and OS support (Linux)
Requires an S-Mode implementation
Sv32
  32bit Virtual Address
  4KiB, 4MiB page tables (2 Levels)
Sv39 (requires an RV64 implementation)
  39bit Virtual Address
  4KiB, 2MiB, 1GiB page tables (3 Levels)
Sv48 (requires an RV64 implementation)
  48bit Virtual Address
  4KiB, 2MiB, 1 GiB, 512GB page tables (4 Levels)
Page Tables also contain access permission
attributes
0xFFFF_FFFF
0x0000_0000
Virtual Address
Virtual Address Map
0xFFFF_FFFF
0x0000_0000
Physical Address
Physical Address Map

## Slide 94: Physical Memory Protection (PMP)
Can be used to enforce access
restrictions on less privileged modes
– Machine Mode can Prevent Supervisor and User Mode software from accessing unwanted memory
Up to 16 regions with a minimum region size of 4 bytes
Ability to Lock a region
  A locked region enforces permissions on all accesses, including M-Mode i.e. none of the mode will be able to gain access here
  Only way to unlock a region is a
Reset
0xFFFF_FFFF
0x0000_0000
4 Byte Regio Only accessi reset
User Mode h RWX Privileg
User Mode h only Privileg
n Locked. |  | 
 |  | Locked Region
le after a |  | 
as full |  | User Mode
s |  | Context
as Read |  | User Mode Data
s |  | 
as |  | Shared Library
 |  | Code
User Mode h Execute only Privileges
Example PMP Memory Map
Can define entire address map as not accessible
to U-Mode in 1 register
If USER mode tries to enter other regions apart from grey zones then the software will then TRAP to machine mode

## Slide 95: RISC-V Interrupts
RISC-V defines the following interrupts per Hart/ Core
  Software – architecturally defined software interrupt
  Timer – architecturally defined timer interrupt
  External – Peripheral Interrupts
  Local – Hart/Core specific Peripheral Interrupts i.e. specific to a particular core
Optionally per privilege level
  Can have Supervisor Software/Timer/Machine Interrupts
  Can have User Software/Timer/Machine
Local interrupts are optional and implementation specific
  Can be used for hart-specific peripheral interrupts
  Useful for latency-sensitive embedded systems or small embedded systems with a small number of interrupts
For more Details Refer: https://five-embeddev.com/quickref/interrupts.html

## Slide 96: Machine Status (mstatus) – As it relates to Interrupts
Bits | Field Name | Description
0 | UIE | User Interrupt Enable
1 | SIE | Supervisor Interrupt Enable
2 | Reserved | 
3 | MIE | Machine Interrupt Enable
4 | UPIE | User Previous Interrupt Enable
5 | SPIE | Supervisor Previous Interrupt Enable
6 | Reserved | 
7 | MPIE | Machine Previous Interrupt Enabler
8 | SPP | Supervisor Previous Privilege
[10:9] | Reserved | 
[12:11] | MPP | Machine Previous Privilege
Bits Field Name | Description
[14:13] FS | Floating Point State
[16:15] XS | User Mode Extension State
17 MPRIV | Modify Privilege (access memory as MPP)
18 SUM | Permit Supervisor User Memory Access
19 MXR | Make Executable Readable
20 TVM | Trap Virtual memory
21 TW | Timeout Wait (traps S-Mode wfi)
22 TSR | Trap SRET
[23:30] Reserved | 
[31] SD | State Dirty (FS and XS summary bit)
RV32 mstatus CSR
M/S/U IE – Global Interrupt Enables for Modes which supports interrupts
M/S/U PIE – Encodes the state of interrupt enables prior to an interrupt.
  These bits can also be written to in order to enable interrupts when returning to lower privilege modes
M/S PP – Encodes the privilege level prior to the previous interrupt
  These bits can also be written to in order to enter a lower privilege mode when executing MRET or SRET instructions
Interrupt Specific Bits for different Modes

## Slide 97: Machine Interrupt Cause CSR (mcause)
Interrupts are identified by reading the
mcause CSR
The Interrupt field determines if a trap was caused by an interrupt or an exception
Interrupt = 1 (interrupt) | 
Exception Code | Description
0 | User Software Interrupt
1 | Supervisor Software Interrupt
2 | Reserved
3 | Machine Software Interrupt
4 | User Timer Interrupt
5 | Supervisor Timer Interrupt
6 | Reserved
7 | Machine Timer Interrupt
8 | User External Interrupt
9 | Supervisor External Interrupt
10 | Reserved
11 | Machine External Interrupt
12 - 15 | Reserved
≥16 | Local Interrupt X
Interrupt = 0 (exception) | 
Exception Code | Description
0 | Instruction Address Misaligned
1 | Instruction Access Fault
2 | Illegal Instruction
3 | Breakpoint
4 | Load Address Misaligned
5 | Load Access Fault
6 | Store/AMO Address Misaligned
7 | Store/AMO Access Fault
8 | Environment Call from U-mode
9 | Environment Call from S-mode
10 | Reserved
11 | Environment Call from M- mode
12 | Instruction Page Fault
13 | Load Page Fault
14 | Reserved
15 | Store/AMO Page Fault
≥16 | Reserved
Bits | Field Name | Description
XLEN-1 | Interrupt | Identifies if an interrupt was synchronous or asynchronous
[XLEN-2:0] | Exception Code | Identifies the exception
mcause CSR

## Slide 98: Machine Interrupt-Enable and Pending CSRs (mie, mip)
mie used to enable/disable a given interrupt
mip indicates which interrupts are currently pending
  Can be used for polling
Lesser-privilege bits in mip are writeable
  i.e. Machine-mode software can be used to generate a supervisor interrupt by setting the STIP bit
mip has the same mapping as mie
Bits | Field Name | Description
0 | USIE | User Software Interrupt Enable
1 | SSIE | Supervisor Software Interrupt Enable
2 | Reserved | 
3 | MSIE | Machine Software Interrupt Enable
4 | UTIE | User Timer Interrupt Enable
5 | STIE | Supervisor Timer Interrupt Enable
6 | Reserved | 
7 | MTIE | Machine Timer Interrupt Enable
8 | UEIE | User External Interrupt Enable
9 | SEIE | Supervisor External Interrupt Enable
10 | Reserved | 
11 | MEIE | Machine External Interrupt Enable
12-15 | Reserved | 
≥16 | LIE | Local Interrupt Enable
mie CSR

## Slide 99: Machine Trap Vector CSR (mtvec)
mtvec sets the Base interrupt vector and the interrupt Mode
mtvec.Mode = Direct
  All Interrupts trap to the address mtvec.Base
  Software must read the mcause CSR and react accordingly
mtvec.Mode = Vectored
  Interrupts trap to the address mtvec.Base + (4*mcause.ExCode)
  Eliminates the need to read mcause for asynchronous exceptions
Bits | Field Name | Description
[XLEN-1:6] | Base | Machine Trap Vector Base Address. 64-byte Alignment
[1:0] | Mode | MODE Sets the interrupt processing mode.
mtvec CSR
mtvec Modes |  | 
Value | Name | Description
0x0 | Direct | All Exceptions set PC to mtvec.BASE Requires 4-Byte alignment
0x1 | Vectored | Asynchronous interrupts set pc to mtvec.BASE + (4×mcause.EXCCODE) Requires 4-Byte alignment
> 0x01 |  | Reserved

## Slide 100: Trap Handler – Entry and Exit
On entry, the RISC-V hart will
– Save the current state
– PC is Copied to Machine Exception Program Counter
– Privilege mode is Copied to M Status Prev. Priv. Mode
– Int. EN is Copied to Machine Status Previous Int. EN
– Then set PC = mtvec (address), mstatus.MIE = 0(to disable Interrupt)
– At this Point we are in Trap Handler
MRET instruction restores state
Typical trap handler software will
PC
Priv
MIE
MEPC
mstatus.MPP
mstatus.MPIE
Push Registers
…
interrupt = mcause.msb if interrupt
branch isr_handler[mcause.code] else
branch exception_handler[mcause.code]
…
Pop Registers MRET
Interrupt handler pseudo code
mtevc.MODE = Direct
PC
Priv
MIE
MEPC
mstatus.MPP
mstatus.MPIE
Stacking
determine type of Int.
Machine Return and Unstacking

## Slide 101: Flow

## Slide 102: Interrupt Handler Code
.align 2
.global trap_entry trap_entry:
addi sp, sp, -16*REGBYTES
//store ABI Caller Registers STORE x1, 0*REGBYTES(sp) STORE x5, 2*REGBYTES(sp)
…
STORE x30, 14*REGBYTES(sp) STORE x31, 15*REGBYTES(sp)
//call C Code Handler call handle_trap
//restore ABI Caller Registers
LOAD x1, 0*REGBYTES(sp)
LOAD x5, 2*REGBYTES(sp)
…
LOAD x30, 14*REGBYTES(sp) LOAD x31, 15*REGBYTES(sp)
addi sp, sp, 16*REGBYTES mret
void handle_trap()
{
unsigned long mcause = read_csr(mcause); if (mcause & MCAUSE_INT) {
//mask interrupt bit and branch to handler
isr_handler[mcause & MCAUSE_CAUSE] ();
} else {
//branch to handler exception_handler[mcause]();
}
}
//write trap_entry address to mtvec
write_csr(mtvec, ((unsigned long)&trap_entry));
RISC-V Assembly interrupt handler to Push and Pop register file
C Code Handler determines interrupt cause and branches to the appropriate function
Step 1
Step 2
Step 3
Step 4
Step 5

## Slide 103: Compiler Interrupt Attribute
Pushing and Popping Registers in Assembly
is a pain
The interrupt attribute was added to GCC to facilitate interrupt handlers written entirely in C
Interrupt functions only saves/restores necessary registers onto the stack
Align function on an 8-byte boundary
Calles MRET after popping register file back
off the stack
void handle_trap(void) attribute((interrupt));
void handle_trap()
{
unsigned long mcause = read_csr(mcause);
if (mcause & MCAUSE_INT) {
//mask interrupt bit and branch to handler isr_handler[mcause & MCAUSE_CAUSE] ();
} else {
//synchronous exception, branch to handler exception_handler[mcause & MCAUSE_CAUSE]();
}
}
//write handle_trap address to mtvec write_csr(mtvec, ((unsigned long)&handle_trap));
Interrupt handler with interrupt attribute.
No assembly Code necessary

## Slide 104: RISC-V Global Interrupts
37
RISC-V defines Global Interrupts as a Interrupt which can be routed to any hart in a system
Global Interrupts are prioritized and distributed by the Platform Level Interrupt Controller (PLIC)
The PLIC is connected to the External Interrupt signal for 1 or more harts in an implementation

## Slide 105: PLIC Interrupt Code Example
In this example an interrupt is presented to the PLIC
The PLIC signals an interrupt to a hart using the Machine External Interrupt (interrupt 11)
The interrupt handler (handle_trap) branches to the defined function to handle the Machine External Interrupt
  C Code placed the address of machine_external_interrupt function in location 11 of the async_handler vector table
The machine_external_interrupt handler does the following:
  Reads the PLIC’s claim/complete register to determine highest priority pending interrupt
  Uses another vector table to branch to the interrupt’s specific handler
  Completes the interrupt by writing the interrupt number back to the PLIC’s claim/complete
void handle_trap(void) attribute((interrupt));
void handle_trap()
{
unsigned long mcause = read_csr(mcause); if (mcause & MCAUSE_INT) {
//mask interrupt bit and branch to handler isr_handler[mcause & MCAUSE_CAUSE] ();
} else {
//synchronous exception, branch to handler exception_handler[mcause & MCAUSE_CAUSE]();
}
}
//install PLIC handler at MEIP Location isr_handler[11] = machine_external_interrupt;
//write trap_entry address to mtvec write_csr(mtvec, ((unsigned long)&handle_trap));
void machine_external_interrupt()
{
//get the highest priority pending PLIC interrupt uint32_t int_num = plic.claim_comlete;
//branch to handler plic_handler[int_num]();
//complete interrupt by writing interrupt number
back to PLIC
plic.claim_complete = int_num;
}

## Slide 106: RISC-V Interrupt System Architecture (M-mode only example)
Core Local Interruptor(CLINT) is a memory mapped peripheral used to generate Software and Timer Interrupts
The Platform Level Interrupt Controller(PLIC) handles the majority of the Core Complex’s Interrupts
  The PLIC has a programmable number prioritization levels
  Only the highest priority pending interrupt is presented on the claim/complete register
Multi-Core interrupt distribution
  The PLIC is globally addressable and is connected to the Machine External Interrupt signal of all cores in the Core Complex